## Slide 2: 2N® Clip
The 2N® Clip is a new 4″ video IP indoor station designed to meet the rising demand for more affordable housing.

## Slide 3: Perfect for mid-range projects
The 2N® Clip was designed with the mid-range sector in mind. You’ll get IP video, good design, and the reliability of 2N's products without the premium price tag

## Slide 4: Increase security. Upgrade to IP video
Forget blurry videos from outdated analog units - high-quality IP video is the new norm in modern living and is much more secure. Meet the market’s standards with the 2N® Clip!

## Slide 5: Fits seamlessly into the 2N ecosystem
The 2N® Clip runs on the powerful, reliable 2N OS – the same as the most premium of products from our workshop. Plus, it can be remotely managed and configured via the My2N Management Platform

## Slide 6
Choose a variant with a built-in induction loop for projects where accessibility is a priority
Save money on a traditional doorbell. Simply connect the doorbell button to the 2N® Clip directly
Drill in two screws and ‘clip’ the 2N® Clip to the wall! This is the fastest indoor station installation
Install it in 3 minutes!
Doorbell button support
Help the hearing-impaired

## Slide 7: Technical parameters
Power supply | 
Type | PoE
PoE | 802.3af Class 0, 48 V DC, 200 mA
User interface | 
Controls | 3 capacitive buttons
Operation | press and hold the RESET button to restore factory settings
Audio | 
Microphone | integrated
Speaker | integrated, 2W
Integrated induction loop | optional
Codecs | G.711a/u, G.722, G.729, L16/16 kHz
Video | 
Display | 4.3” display
Resolution | 480x272 pixels
Codecs | H.264
Interface | 
LAN | 10/100BaseT, RJ-45
Recommended cabling | Cat5e or higher
Doorbell input | 
Input type | switching contact (button/relay)
Contact type | normally open (NO)
Contact parameters | 12V/20mA, DC
Mechanical properties | 
Operating temperature | 0 to 50°C
Storage temperature | -20 to 70°C
Relative operating humidity | 10 to 90 % (non-condensing)
Recommended altitude | 0 to 2000 m
Dimensions | 124 (W) x 150 (H) x 28 (D) mm
Weight | 235 g

## Slide 8: E2E mid-range solution
Bring premium quality to mid-priced residential projects
With the 2N® Clip in your portfolio, you can easily offer comprehensive 2N solution even to the price sensitive projects

## Slide 9: Order numbers
9138511
9138002
2N Clip Desk Stand
9138512
2N® Clip, Ethernet, Induction Loop
2N® Clip, Ethernet

## Slide 10: Answering unit portfolio
High-end 7” full screen
Mobile
High-end 4” video
Cost effective
Premium audio only
Home Automation
Cost effective video

## Slide 11: Bring the power of IP to every home